| Ravello Dual CCT LED Wall Exterior Wall Lighting |  | Data Sheet |
| --- | --- | --- |
| Product Information The Ravello Dual CCT LED wall light is perfect for down lighting and wall washing both internal & external walls. A stand-alone unit or a choice of 2 shade styles to suit most installations. Comes with a 2 year warranty for your peace of mind. |  | Product Features 2 year warranty Class I IP65 Dual CCT 3000K & 4000K 650lm – 3000K 730lm – 4000K CRI>Ra90 2 Shade designs to choose from Cone or Sleek Shade L70 - 30,000 hours Non dimmable Integrated driver |

Product Specification

| Product Code | Product Description | Wattage (W) | CCT (K) | Lumens (lm) | CRI (Ra) | Energy Efficiency Class | Protection Class |
| --- | --- | --- | --- | --- | --- | --- | --- |
| KSR71100 | Ravello Dual CCT 7.5W Anthracite LED Wall Light | 7.5 | 3000 | 650 | 91 | F | I |
|  |  | 7.5 | 4000 | 730 | 90 | F | I |
| KSR71102 | Ravello I Sleek Shade |  |
| KSR71103 | Ravello II Cone Shade |  |
| Nominal voltage | 220~240VAC |
| Operating frequency | 50-60Hz |
| Circuit Power 3K / 4K | 9.23W including driver losses / 9.02W including driver losses |
| Circuit Current | 0.043A |
| PFC | 0.87 |
| Ambient temperature range | 0°c~+35°c |
| Start time | < 0.5 sec |
| IP rating | 65 |

Construction

| Body: | Cast Aluminium |
| --- | --- |
| Lens: | Glass |
| Shades: | Cast Aluminium |

Standards

| BSEN60598-1:2021 | Luminaires – Part 1: General requirements and tests |
| --- | --- |

In Conformity with

| LVD | Low voltage directive 2014/35/EU |
| --- | --- |
| EMC | Electromagnetic compatibility directive 2014/30/EU |
| ERP | Energy related products directive 2019/2020/EU |
| RoHS | Restriction of hazardous substances 2015/863/EU |

Product Dimensions

KSR Lighting is constantly developing and improving its products. For this reason, all product descriptions in this data sheet are intended as a general guide, and KSR may change specifications from time to time in the interest of product development, without prior notification or public announcement. All descriptions in this data sheet present only general particulars of the goods to which they refer and shall not form part of any contract. Data in this guide has been obtained in controlled experimental conditions. However, KSR Lighting cannot accept any liability arising from the reliance on such data to the extent permitted.