| Positano Range Exterior Wall & Bollard Lighting |  | Data Sheet |
| --- | --- | --- |
| Product Information The Positano range is perfect for a multitude of exterior applications where a decorative finish is desired. The range is available as 2 sized wall versions and 2 decorative bollard heights to match. Supplied as dual CCT as standard and all in an anthracite finish. |  | Product Features 3-year warranty Class I IP65 Supplied as Dual CCT – 3000K or 4000K CRI: >80 3.2W or 6.5W LED Strong Cast Aluminium Body Family of Wall lights and matching Bollards Loop in / Loop out L70 - 30,000hrs |

Product Specification

| Product Code | Product Description | Wattage (W) | CCT (K) | Lumens (lm) | CRI (Ra) | Energy Efficiency Class | Protection Class |
| --- | --- | --- | --- | --- | --- | --- | --- |
| KSR71110 | Positano S 3.2W LED Down Wall Light | 3.2W | 3000 | 120 | >80 | E | I |
|  |  | 3.2W | 4000 | 115 |  |  |  |
| KSR71111 | Positano M 6.5W LED Down Wall Light | 6.5W | 3000 | 230 | >80 | F | I |
|  |  | 6.5W | 4000 | 240 |  |  |  |
| KSR71112 | Positano 3.2W 400mm LED Bollard | 3.2W | 3000 | 120 | >80 | E | I |
|  |  | 3.2W | 4000 | 115 |  |  |  |
| KSR71113 | Positano 3.2W 750mm LED Bollard | 3.2W | 3000 | 120 | >80 | E | I |
|  |  | 3.2W | 4000 | 115 |  |  |  |
| Technical Data | Positano S wall light | Positano M wall light | Positano Bollards |
| Nominal voltage | 220~240VAC | 220~240VAC | 220~240VAC |
| Operating frequency | 50/60Hz | 50/60Hz | 50/60Hz |
| Circuit Wattage – 3K / 4K | 4.26W / 4.23W Both including driver losses | 7.95W / 8.11W Both including driver losses | 4.26W / 4.23W Both including driver losses |
| Circuit Current | 0.033A / 0.033A | 0.044A / 0.043A | 0.033A / 0.033A |
| Driver mA Rating | TBC | TBC | TBC |
| PFC | 0.516 / 0.516 | 0.742 / 0.746 | 0.516 / 0.516 |
| In Rush Current | 0.175A / -2.3A | -1.15A / -2.04A | 0.175A / -2.3A |
| Ambient temperature range | 0°c to +30°c | 0°c to +30°c | 0°c to +30°c |
| IP rating | 65 | 65 | 65 |

Construction

| Body: | Cast Aluminium |
| --- | --- |

Standards

| BSEN60598-1:2021 | Luminaires – Part 1: General requirements and tests |
| --- | --- |

In Conformity with

| LVD | Low voltage directive 2014/35/EU |
| --- | --- |
| EMC | Electromagnetic compatibility directive 2014/30/EU |
| ERP | Energy related products directive 2019/2020/EU |
| RoHS | Restriction of hazardous substances 2015/863/EU |

Product Dimensions

KSR71110

KSR71111

KSR71112

KSR71113

KSR Lighting is constantly developing and improving its products. For this reason, all product descriptions in this data sheet are intended as a general guide, and KSR may change specifications from time to time in the interest of product development, without prior notification or public announcement. All descriptions in this data sheet present only general particulars of the goods to which they refer and shall not form part of any contract. Data in this guide has been obtained in controlled experimental conditions. However, KSR Lighting cannot accept any liability arising from the reliance on such data to the extent permitted.